## Slide 1: Computer Organization and Assembly Fall 2019
Lecture 14 & 15
Syeda Farwa Batool

## Slide 2: String Instructions
Instructions that can process blocks of data in one go. They are called block processing or string instructions.
String instructions work on a block of data. A block has a start and an end. The instructions can work from the start towards the end and from the end towards the start.
Every string instruction has two variants
  word
  byte

## Slide 3: Direction Flag
The direction of movement is controlled with the Direction Flag (DF) in the flags register.
If this flag is cleared (DF = 0) the direction is from lower addresses towards higher addresses If DF is cleared, this is called the auto increment mode of string instruction
If this flag is set (DF = 1) the direction is from higher addresses to lower addresses. if DF is set, this is called the auto decrement mode. There are two instructions to set and clear the direction flag.
cld ; clear direction flag
std ; set direction flag

## Slide 4: STOS [stosw or stosb]
STOS transfers a byte or word from register AL or AX to the string element addressed by ES:DI and updates DI to point to the next location.
The implied source will always be in AL or AX. If DF is clear, DI will be incremented by one or two depending of whether STOSB or STOSW is used.
DF = 0 DI = DI + 2 if word operation
  DI = DI + 1 if byte operation
If DF is set DI will be decremented by one or two depending of whether STOSB or STOSW is used.
DF = 1 DI = DI - 2 if word operation
  DI = DI - 1 if byte operation
Memory Location ES:DI
AX/AL Register
Memory Location ES:DI
AX/AL Register

## Slide 5: STOS Example 1 Clear whole screen [from start of screen]
clrscr:
pushf
pusha
push es
mov ax, 0xb800
mov es, ax ; point es to video base
xor di, di ; point di to top left column
mov ax, 0x0720 ; space char in normal attribute
mov cx, 2000 ; number of screen locations
L1:
stosw ;; mov [es:di] , ax add di ,2
loop L1
pop es
popa
popf
ret
By default DF = 0, means DI will be incremented

## Slide 6: STOS Example 2 Clear whole screen [from end of screen]
clrscr:
pushf
pusha
push es
mov ax, 0xb800
mov es, ax ; point es to video base
std; ; set direction DF = 1
mov di, 4000 ; point di to bottom right column
mov ax, 0x0720 ; space char in normal attribute
mov cx, 2000 ; number of screen locations
L1:
stosw ;; mov [es:di] , ax sub di ,2
loop L1
pop es
popa
popf
ret
DF = 1, means DI will be Decremented

## Slide 7: LODS [lodsw or lodsb]
LODS transfers a byte or word from the string element addressed by DS:SI to register AL or updates SI to point to the next location.
The implied destination will always be in AL or AX. If DF is clear, SI will be incremented by one or two depending of whether LODSB or LODSW is used.
DF = 0 SI = SI + 2 if word operation
  SI = SI + 1 if byte operation
If DF is set SI will be decremented by one or two depending of whether LODSB or LODSW is used
DF = 1 SI = SI - 2 if word operation
  SI = SI - 1 if byte operation
Memory Location DS:SI
AX/AL Register
AX/AL
Register
Memory Location DS:SI

## Slide 8: LODS Example 1 load each character of string in register AX
print:
pushf
pusha
push es
;; our segment (DS )value is already set
mov si, str ; point si to starting location of string
lodsb ;; mov al, [ds:si] , add si , 1
L1:
    cmp al ,0
    Je end
    lodsb ;; mov al, [ds:si] , add si , 1
Jmp L1
end:
pop es
popa
popf
ret
str: db "Pakistan",0
By default DF = 0, means SI will be incremented

## Slide 9: LODS Example 2 Print loaded character of previous example on screen
print:
pushf
pusha
push es
;; our segment (DS )value is already set
mov ax, 0xb800
mov es, ax ; point es to video base
xor di, di ; point di to top left column
mov si, str ; point si to starting location of string
mov ah,07 ;; load normal attribute in higher part of register
lodsb ;; mov al, [ds:si] , add si , 1
L1:
    cmp al ,0
    Je end
    stosw ;; mov [es:di] , ax add di , 2
    lodsb ;; mov al, [ds:si] add si , 1
    Jmp L1
end:
pop es
popa
popf
ret
str: db "Pakistan",0

## Slide 10: Class Activity
Write a program that prints reverse of a string, staring from top left column of screen
For Example
  Str: db “Pakistan”,0
  It should prints like :
  natsikaP
2. Write a program that prints a string on right bottom column of screen
For Example
  Str: db “Pakistan”,0
  It should prints like :
Pakistan

## Slide 11: REP Prefix
REP repeats the following string instruction CX times. The use of CX is implied with the REP prefix. The decrement in CX doesn’t affect any flags and the jump is also independent of the flags

## Slide 12: REP Example Clear whole screen [from start of screen]
clrscr:
pushf
pusha
push es
mov ax, 0xb800
mov es, ax ; point es to video base
xor di, di ; point di to top left column
mov ax, 0x0720 ; space char in normal attribute
mov cx, 2000 ; number of screen locations
rep stosw ;; mov [es:di] , ax add di ,2
pop es
popa
popf
ret
By default DF = 0, means DI will be incremented

## Slide 13: MOVS [movsw or movsb]
MOVS transfers a byte or word from the source location DS:SI to the destination ES:DI and updates SI and DI to point to the next locations.
The implied destination will always be in ES:DI. If DF is clear, SI and DI will be incremented by one or two depending of whether MOVSW or MOVSB is used.
if word operation
DF = 0 SI = SI + 2
  DI = DI + 2
If DF is set SI and DI will be decremented by one or two depending of whether MOVSW or MOVSB is used
DF = 1 if word operation
    SI = SI - 2
      DI = DI - 2
Memory Location DS:SI
Memory Location ES:DI
Memory Location DS:SI
Memory Location ES:DI

## Slide 14: MOVS Example copy string on video memory
print:
pushf
pusha
push es
;; our segment (DS )value is already set
mov ax, 0xb800
mov es, ax ; point es to video base
xor di, di ; point di to top left column
mov si, str ; point si to starting location of string
mov cx, [length]
rep movsw
;; what above instructions do
;; mov [es:di] , [ds:si]
;; add di 2
;; add si,2
;; repert it for cx times
pop es
popa
popf
ret
length: dw 8
str: dw
0x0750,
0x0761,
0x076b,
0x0769,
0x0773,
0x0774,
0x0761,
0x076E
;Pakistan

## Slide 15: Class Activity
You have two string in data segment. Append the content of first string at the end of last string (hint: use movs instruction )
  Length1: dw 8
  Length2: dw 13
  str1: db “Pakitan”
  str2: db “Lahore is in “
After execution of your code str2 becomes “Lahore is in Pakistan”

## Slide 16: SCAS [scasw or scasb]
SCAS compares a source byte or word in register AL or AX with the destination string element addressed by ES:DI and updates the flags. DI is updated to point to the next location.
If DF is clear, DI will be incremented by one or two depending of whether SCASW or SCASB is used.
if word operation
DF = 0 DI = DI + 2
if byte operation
DI = DI + 1
If DF is set, DI will be decremented by one or two depending of whether SCASW or SCASB is used.
if word operation
DF = 1 DI = DI - 2
if byte operation
DI = DI - 1
AL/ AX
Memory Location ES:DI
Memory Location ES:DI
Compare to
AL/ AX
Compare to

## Slide 17: REPE and REPNE Prefixes
REPE or REPZ repeat the following string instruction while the zero flag is set ZF = 1
REPNE or REPNZ repeat the following instruction while the zero flag is not set. ZF = 0

## Slide 18: REPNE + SCAS Example Calculate length of string
length:
pushf
pusha
push es
;; Our string is in Data segment but we can iterate over extra segment, while using SCAS inst
push ds
pop es
mov cx, 0xffff ; load maximum number in cx
mov di, str ; point di to starting location of string
xor al,al ;; load 0 in al so scacs can work
repne scasb ;; scasb will compare al and byte[es:di] and increment di by 1
;; repne will decrement cx value
mov ax, 0xffff
sub ax,cx ;; length of string is in AX register
pop es
popa
popf
ret
str: db "Pakistan",0

## Slide 19: CMPS
CMPS subtracts the source location DS:SI from the destination location ES:DI. Source and Destination are unaffected. SI and DI are updated accordingly.
If DF is clear, SI and DI will be incremented by one or two depending of whether CMPSW or CMPSB is used.
if word operation
DF = 0 SI = SI + 2
  Compare to DI = DI + 2
If DF is set SI and DI will be decremented by one or two depending of whether CMPSW or CMPSB is used
DF = 1 if word operation
    Compare to SI = SI - 2
      DI = DI - 2
Memory Location DS:SI
Memory Location ES:DI
Memory Location DS:SI
Memory Location ES:DI

## Slide 20: CMPS Example [Check two string are equal or not]
compare:
pushf
pusha
push es
;; our segment (DS )value is already set
mov si, str1
;; our second string is also DS so our es should contain DS value
push ds ;; mov ax,ds
pop es ;; mov es,ax
mov di,str2
;; For this case just assume length of both strings are equall
mov cx, [length]
inc cx

## Slide 21: continue
repe cmpsb
jcxz equall ;; jmp taken if CX = 0
mov ax,0 ;; means they are not equal
jmp end
equall:
mov ax,1 ;; means they are equal
end:
pop es
popa
popf
ret
length: dw 8
str1: db "Pakistan"
str2: db "PaKistan"

## Slide 22: LES Instruction
LES loads ES.
It have two parameters, one is the general purpose register to be loaded and the other Is the memory location from which to load these registers.
For example
Les di, [offsValueANDSegmentValue] ;
; this is do following work
Mov di, [offsValueANDSegmentValue]
Mov es, [offsValueANDSegmentValue + 2]

## Slide 23: LDS Instructions
LDS loads DS.
It have two parameters, one is the general purpose register to be loaded and the other Is the memory location from which to load these registers.
For example
Lds si, [offsValueANDSegmentValue] ;
; this is do following work
Mov si, [offsValueANDSegmentValue]
Mov ds, [offsValueANDSegmentValue + 2]

## Slide 24: Class Activity
Write a subroutine that receives 6 values, offset and segment of string1 and then offset and segment of string2 respectively and then length of string (assume both strings are equal). Function will return 1 if string1 and string2 are equal other wise zero.
C++ version can be
Bool compare(int str1_offset, int str1_seg, int str2_offset, int str2_seg, length )