## Slide 1: Computer Organization and Assembly Fall 2019
Lecture 22
Syeda Farwa Batool

## Slide 2: What Is Pipelining?
Pipelining is an implementation technique whereby multiple instructions are overlapped in execution.
It takes advantage of parallelism that exists among the actions needed to execute an instruction.
Today, pipelining is the key implementation technique used to make fast CPUs.
Courtesy by Miss Noshaba

## Slide 3: Real World Analogy
A pipeline is like an assembly line.
In an automobile manufacturing line, there are many steps, each contributing something to the construction of the car.
Each step operates in parallel with the other steps, although on a different car.
Courtesy by Miss Noshaba

## Slide 4: Real World Analogy
Automobile manufacturing line without pipelining, in 3 stages
Assemble (A), Paint (P), Fix tires (T)
Assuming A+P+T take 3 hours
Time line | 0-3 hours | 3-6 Hours | 6 -9Hours
Car 1 | A+P+T |  | 
Car 2 |  | A+P+T | 
Car 3 |  |  | A+P+T
Courtesy by Miss Noshaba

## Slide 5: Real World Analogy
Automobile manufacturing line with pipelining, in 3 stages
Assemble (A), Paint (P), Fix tires (T)
It takes 5 hours with pipelining and 9hours without pipelining
Speedup = 9/5
Time line | 1st hour | 2nd hour | 3rd hour | 4th hour | 5th hour | 6th hour | 7th hour | 8th hour | 9th hour
Car 1 | A | P | T |  |  |  |  |  | 
Car 2 |  | A | P | T |  |  |  |  | 
Car 3 |  |  | A | P | T |  |  |  | 
Courtesy by Miss Noshaba

## Slide 6: Real World Analogy
Here our assumptions are
  There is no time consumed to transition car from one working station on other
  All the stages consume equal time
However these assumption are not valid
  Each stage can take different amount of time
    For example painting a car takes 2 hours and Assembly and installing types take 0.5 hours each
  To transfer car from one stage to another will take time.
    For example, it takes 10 minutes to transfer a car from Assembly room to paint rooms and 10 minute to transfer from paint room to tire fixing room.
    Note that this will not be consume in un-pipeline factory as everything will be done is same room
Courtesy by Miss Noshaba

## Slide 7: Real World Analogy
Automobile manufacturing line with pipelining, in 3 stages
If Assemble (A), Paint (P), Fix tires (T) take different time
If Assembly take 0.5 hour, Paint 2 hours and Tires 0.5 hours
  Paint of Car2 cannot start before 2.5th hour because Paint unit is busy with Car1. So after Assembly Car 2 has to wait for 1.5 Hours
  Total time take to complete 3 instructions =7h
Speed Up = 9/7
Time line | 0-0.5h | 0.5-2.5h | 2.5-4.5h | 4.5-6.5 h | 6.5-7 h
Car 1 | A (0.5 h) | P (2h) | T (0.5h) |  | 
Car 2 |  | A (0.5 h) +wait for 1.5 h | P (2h) | T (0.5h) | 
Car 3 |  |  | A (0.5h)+ wait for 1.5 h | P (2h) | T (0.5h)
Courtesy by Miss Noshaba

## Slide 8: Real World Analogy
Automobile manufacturing line with pipelining, in 3 stages
If we add time for transition between stages as well
Total time taken to complete 3 instructions = 7h+0.67h=7.67
Speed Up = 9/7.67
Time line | 0-0.5h | Transition time 10 min | 0.5-2.5h | Transition time 10 min | 2.5-4.5h | Transition time 10 min | 4.5-6.5 h | Transition time 10 min | 6.5-7 h
Car 1 | A (0.5 h) |  | P (2h) |  | T (0.5h) |  |  |  | 
Car 2 |  |  | A (0.5 h) +wait for 1.5 h |  | P (2h) |  | T (0.5h) |  | 
Car 3 |  |  |  |  | A (0.5h)+ wait for 1.5 h |  | P (2h) |  | T (0.5h)
Courtesy by Miss Noshaba

## Slide 9: CISC
CISC, which stands for Complex Instruction Set Computer.  Each instruction executes multiple low level operations.  Ex. A single instruction can load from memory, perform an arithmetic operation, and store the result in memory.  Smaller program size. CISC
CISC Characteristics  A large number of instructions.  Some instructions for special tasks used infrequently.  A large variety of addressing modes (5 to 20).  Variable length instruction formats. Disadvantages : However, it soon became apparent that a complex instruction set has a number of disadvantages:  These include a complex instruction decoding scheme, an increased size of the control unit, and increased logic delays.

## Slide 10
RISC  RISC Stands for Reduced Instruction Set Computer.  It is a microprocessor that is designed to perform a smaller number of types of computer instruction so that it can operate at a higher speed.
RISC Characteristics
Relatively few instructions 128 or less  Relatively few addressing modes.
Memory access is limited to LOAD and STORE instructions. All operations done within the registers of the CPU.  This architectural feature simplifies the instruction set and encourages the optimization of register manipulation.  An essential RISC philosophy is to keep the most frequently accessed operands in registers and minimize register-memory operations.
RISC Characteristics Cont..  Fixed Length, easily decoded instruction format  Typically 4 bytes in length  Single cycle instruction execution  Done by overlapping the fetch, decode and execute phases of two or three instructions known as Pipelining!!  Large number of registers in the processor unit.  Use of overlapped Register Windows.

## Slide 11: Instruction Execution Cycle
Obtain instruction from program storage
Determine required actions and obtain operand data
Locate and obtain operand data
Load or Store values in memory
Deposit results in register for later use
Instruction
Decode
Instruction
Fetch
Execute
Writeback
Result
Memory
Courtesy by Sir Haroon

## Slide 12: 1st and 2nd Instruction cycles
Instruction fetch (IF)
  IR (instruction register) Mem[PC];
  NPC (next PC) PC + 4
Instruction decode & register fetch (ID)
  A Regs[IR21..25];
  B Regs[IR16..20];
Courtesy by Sir Haroon

## Slide 13: 3rd Instruction cycle
Execution & effective address (EX)
  Memory reference
    ALUOutput A + Imm
  Register - Register ALU instruction
    ALUOutput A func B
  Register - Immediate ALU instruction
    ALUOutput A op Imm
  Branch
    AddOutput NPC + Imm; Cond (A op B)
Courtesy by Sir Haroon

## Slide 14: 4th Instruction cycle
Memory access
  Memory reference
    PC NPC
    LMD Mem[ALUOutput] (load)
    Mem[ALUOutput] B (store)
Courtesy by Sir Haroon

## Slide 15: 5th Instruction cycle
Write-back (WB)
  Register - register ALU instruction
    Regs[IR11..15] ALUOutput
  Register - immediate ALU instruction
    Regs[IR16..20] ALUOutput
  Load instruction
    Regs[IR16..20] LMD
Courtesy by Sir Haroon

## Slide 16: Pipeline
A
Start and finish a job before moving to the next
Time
Jobs
Break the job into smaller stages
B
C
A
B
C
A
B
C
A
B
C
Unpipelined
Pipelined
Courtesy by Sir Haroon

## Slide 17: Pipeline Throughput and Latency
Consider the pipeline above with the indicated delays. We want to know what is the pipeline throughput and the pipeline latency.
Pipeline throughput: instructions completed per second.
Pipeline latency: how long does it take to execute a single instruction in the pipeline.
IF
ID
EX
MEM
WB
5 ns
4 ns
5 ns
10 ns
4 ns
Courtesy by Sir Haroon

## Slide 18: Pipeline Throughput and Latency
Pipeline throughput:
IF
ID
EX
MEM
WB
5 ns
4 ns
5 ns
10 ns
4 ns
Pipeline Instruction latency:
Courtesy by Sir Haroon

## Slide 19: Real World Analogy
Automobile manufacturing line with pipelining, in 3 stages
If we add time for transition between stages as well
Total time taken to complete 3 instructions = 7h+0.67h=7.67
Speed Up = 9/7.67
Time line | 0-0.5h | Transition time 10 min | 0.5-2.5h | Transition time 10 min | 2.5-4.5h | Transition time 10 min | 4.5-6.5 h | Transition time 10 min | 6.5-7 h
Car 1 | A (0.5 h) |  | P (2h) |  | T (0.5h) |  |  |  | 
Car 2 |  |  | A (0.5 h) +wait for 1.5 h |  | P (2h) |  | T (0.5h) |  | 
Car 3 |  |  |  |  | A (0.5h)+ wait for 1.5 h |  | P (2h) |  | T (0.5h)
Courtesy by Miss Noshaba

## Slide 20: Note
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously
Potential speedup = Number of pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
Courtesy by Sir Haroon

## Slide 21: Visualizing Pipelining
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Courtesy by Sir Haroon