## Slide 1: Computer Organization and Assembly Fall 2019
Lecture 5
Syeda Farwa Batool

## Slide 2: Illegal Addressing
mov al , [bl]
mov ax , [bx – si ]
mov ax , [bx + bp]
mov ax , [si + di]
Address can not be 8 bit it has to be 16 bit
Register cannot be subtracted
2 base registers cannot come together in one addressing
2 indices cannot come together in one addressing

## Slide 3: Effective Address
          base + index + offset
bx/bp + si/di + any constant i.e 0x100
But offset + base (effective address) just determine location in segment.
To determine exact location in complete memory, we also need segment address and effective address both.
First compute Effective address then then we are able to get physical address.
Base Address of any memory location
Distance from base address
Notes: BX=0100, SI=0200, and CS=1000 and the memory access
under consideration is [cs:bx+si+0x0700],
EA = 0x0100 + 0x0200 + 0x700
= 0A00
CS = 1000 * 10 = 10000
PA = 10000 + 0A00
= 10A00

## Slide 4: Registers with their default segment
  CS:IP
  DS:BX ==
  DS:SI
  ES:DI
  SS:SP
  SS:BP
[BX] => means to compute physical address use Data Segment (DS) + BX register vales

## Slide 5: Segment Wraparound
In case of Effective Address:
        0
        FFFF
FFFF + 1 = 10000
0000
A segment

## Slide 6: Segment Wraparound
In case of Physical Address:
        0
        FFFF:FFFF
FFF:FFFF + 1 = 10FF0
0FF0
whole Memory

## Slide 7: Branching
Branching means shifting or changing your IP from regular flow.
For example
My next executable instruction address is 0x0300, but I enforce my program to jump to instruction 5 whose address is 0x0500. So this jumping is called branching.
1 0x0100
2 0x0200
3 0x0300
4 0x0400
5 0x0500
IP
IP

## Slide 8: Conditional Jump
Jump to some address, if some condition is true or false.
This is like if/else conditions in high level language.
Every condition in high level language is Boolean expression.
For this purpose in Assembly we have an instruction called cmp

## Slide 9: CMP
Subtract (sub) the source (src) from the destination (dest).
Does not change the content of source or destination.
Affects AF, CF, OF, PF, SF and ZF

## Slide 10: Some Conditional Jumps
Jz – jump if zero
Jnz – jump if not zero
Je – jump if equal
Jne – jump if not equal
Example
cmp ax,bx
jz lable1 ;; if ax and bx are equal ;;then jump to lable 1
Example
cmp ax,bx
jne lable1 ;; if ax and bx are not equal ;;then jump to lable 1

## Slide 11: Some Conditional Jumps
Jc – jump if carry flag is set
Jnc – jump if carry flag is not set
Example
add ax, bx
jc lable1
Example
sub ax,bx
jnc lable1

## Slide 12: Some Conditional Jumps
Ja – jump if dest above src
Jb – jump if dest below src
Unsigned integers
ZF = 0 and CF = 0
CF = 1

## Slide 13: Some Conditional Jumps
Jl – jump if Sdest lower than Ssrc
Jg – jump if dest greater than src
Signed integers
ZF ≠ CF
ZF = 0 and SF = OF

## Slide 14: A program to add ten numbers using base register + index addressing, [Example 1]
;; loop to add 10 elements of array
[org 0x0100]
mov bx, 0 ; initialize array index to zero
mov cx, 10 ; load count of numbers in cx
mov ax, 0 ; initialize sum to zero
mov bx,num1
mov di,0
l1: add ax, [bx+di] ; add number to ax
add di, 2 ; advance di to next index
sub cx, 1 ; numbers to be added reduced
jnz l1 ; if numbers remain add next
mov ax, 0x4c00 ; terminate program
int 0x21
num1: dw 10, 20, 30, 40, 50, 10, 20, 30, 40, 50
total: dw 0

## Slide 15: Convert High level Code to low Level Example 2
//High level language code
int ax = 10;
int bx = 15;
int cx = 0;
if( ax == bx)
{
cx = ax;
}
else
{
cx = bx;
}
;;Assembly language code
mov ax , 10
mov bx , 15
mov cx , 0
cmp ax , bx
jne lable1
mov cx , ax
jmp end
lable1:
mov cx , bx
end:

## Slide 16: Execution of Example 2
;;Assembly language code
mov ax , 15
mov bx , 15
mov cx , 0
cmp ax , bx
jne lable1
mov cx , ax
jmp end
lable1:
mov cx , bx
end:
;;Assembly language code
mov ax , 15
mov bx , 10
mov cx , 0
cmp ax , bx
jne lable1
mov cx , ax
jmp end
lable1:
mov cx , bx
end:

## Slide 17: Try to convert following code in assembly
int ax = 10;
int bx = 15;
int cx = 0;
Int dx = 0; //this will save largest number
if((ax >= bx) && (ax >= cx))
{
  dx = ax;
}
else if ((bx >= ax) && (bx >= cx)) {
dx = bx
}
else {
dx = cx
}
Hint:
If one condition of && (and) is false other is not checked
If ax >= bx is false
Then bx > ax is true