## Slide 1: Computer Organization and Assembly Fall 2019
Lecture 6
Syeda Farwa Batool

## Slide 2: Unconditional Jump
Jump to some instructions without any condition or without referencing any flag.
                Jmp lable1
All Unconditional Jumps can be:
  Short Jump
  Near Jump
  Far Jump
But all conditional Jumps can only
  Short Jump

## Slide 3: Position Relative Jump
Jump instruction opcode has address relative to IP
3 [org 0x0100]
4
5 00000000 EB08 jmp start
6
7 00000002 0A0014001E002800 data: dw 10, 20, 30, 40
8
9 start:
10
11 0000000A A1[0200] mov ax, [data]
12 0000000D 8B1E[0400] mov bx, [data +2]
13
14 00000011 B8004C mov ax, 0x4c00
15 00000014 CD21 int 0x21
08 is offset address where IP has to move
But address of Start label is
010A,
08 is referenced to current location which is 0100,
Means from current location how many bytes we have to skip to reach start label
And we have 4 words
4 * 2 = 8

## Slide 4: Short jump
Short jump is relative to current location or address
In Short jump offset (number of bytes we want to skip) size is 1 byte
So we know signed byte limitation in
And here n= 8
= 127 to +128
Maximum forward jump can be IP+ 127 bytes
Maximum backward jump can be IP – 128 bytes
Short jumps works within a segment
Two’s Complement Range = -2 (n-1) to + (2(n - 1) -1)

## Slide 5: Near jump
Short jump is relative to current location or address
In near jump offset (number of bytes we want to skip) size is 2 byte
So we know signed byte limitation in
And here n= 16
= -32768 to +32767
Maximum forward jump can be IP+ 32767 bytes
Maximum backward jump can be IP – -32768 bytes
Near jumps works within a segment
Two’s Complement Range = -2 (n-1) to + (2(n - 1) -1)

## Slide 6: Far Jump
Far jump is not positon relative
It is an absolute jump
Jump in between segments (Neither near nor short jump can work)
Need segment and offset both
When we jump to some other segment, our code segment and our IP will update according to new segment
Through Following commands we can do far jumps
  Far Jump
  Call
  ret

## Slide 7: Opcodes of Jumps
Jump Type | Opcode
Short Jump | EB
Near Jump | E9
Far Jump | EA