## Slide 1: Computer Organization and Assembly Fall 2019
Lecture 7
Syeda Farwa Batool

## Slide 2: Declare a large Array
;a program to add three numbers using registers
3 [org 0x0100]
4
5 00000000 EB14 jmp start
6
7
8 00000002 4100<rept> arr: times 10 dw 'A'
9
10
11 start:
12
13 00000016 A1[0200] mov ax, [arr + 0]
14
15
16 00000019 B8004C mov ax, 0x4c00 ; terminate program
17 0000001C CD21 int 0x21

## Slide 3: Bubble Sorting in Assembly {unsigned array}
Example 3.3
; sorting a list of ten numbers using bubble sort
[org 0x0100]
jmp start
data: dw 60, 55, 45, 50, 40, 35, 25, 30, 10, 0
swap: db 0

## Slide 4
start:
mov bx, 0 ; initialize array index to zero
mov byte [swap], 0 ; rest swap flag to no swaps
loop1:
mov ax, [data+bx] ; load number in ax
cmp ax, [data+bx+2] ; compare with next number
jbe noswap ; no swap if already in order
mov dx, [data+bx+2] ; load second element in dx
mov [data+bx+2], ax ; store first number in second
mov [data+bx], dx ; store second number in first
mov byte [swap], 1 ; flag that a swap has been done
noswap:
add bx, 2 ; advance bx to next index
cmp bx, 18 ; are we at last index
jne loop1 ; if not compare next two
cmp byte [swap], 1 ; check if a swap has been done
je start ; if yes make another pass
; terminate program lines
First number is greater than second number so swap them
If any swap happens then traverse again

## Slide 5: Bit Manipulation

## Slide 6: Shift Operations
Shift Logical Right (SHR)
Shift Logical Left (SHL) / Shift Arithmetic Left (SAL)
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
CF = 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0
CF = 1
Notes: mov ax, 0xB4
shr ax,1 ;; do one shift operation to right
shr ax , 2 ;; do two shifts operations to right
mov bx, 0xB4
srl bx, 1 ;; do one shift operation to left

## Slide 7: Rotate Operations
Rotate Right (ROR)
Rotate Left (ROL)
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
CF = 0
This was last bit which dropped from right also copied in carry flag
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
CF = 1
This was last bit which dropped from left also copied in carry flag
Notes: mov ax, 0xB4
ror ax,1 ;; do one rotate operation to right
ror ax , 2 ;; do two rotate operations to right
mov bx, 0xB4
srl bx, 1 ;; do one rotate operation to left

## Slide 8: Rotate Through Carry
Rotate Through Carry Right (RCR)
1 | 1 | 0 | 1 | 1 | 0 | 1 | 0
CF = 0
Let the initial value of
CF = 1
Copy CF value to empty place
Last Bit from right is copied to carry flag
Notes: mov ax, 0xB4
rcr ax,1

## Slide 9: Rotate Through Carry
Rotate Through Carry Left (RCL)
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0
CF = 1
Let the initial value of
CF = 0
Copy CF value to empty place
Last Bit from left is copied to carry flag
Notes: mov ax, 0xB4
rcl ax,1

## Slide 10: MULTIPLICATION IN ASSEMBLY LANGUAGE
1101 = 13
0101 = 5
-------------- = 0 (Initial Value)
              1101 = 0 + 13 = 13
              0000x = 13 + 0 = 13
              1101xx = 13 + 52 = 65
              0000xxx = 0 65 + 0 = 65 (Answer)
110100 = 52

## Slide 11: Basic Logic for multiplication
1101 = 13 Multiplicand 0101 = 5 Multiplier 0000 = 0 Result
1) Shift the multiplier to the right.
2) If CF=1 add the multiplicand to the result.
3) Shift the multiplicand to the left.
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
CF = 1
Multiplier
0 | 0 | 0 | 0 | 1 | 1 | 0 | 1
Result
0 | 0 | 0 | 1 | 1 | 0 | 1 | 0
Multiplicand
2
13
26

## Slide 12: Basic Logic for multiplication
11010 = 26 Multiplicand 0010 = 2 Multiplier 1101= 13 Result
1) Shift the multiplier to the right.
2) If CF=1 add the multiplicand to the result.
3) Shift the multiplicand to the left.
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
CF = 0
Multiplier
0 | 0 | 0 | 0 | 1 | 1 | 0 | 1
Result
0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
Multiplicand
0
13
52

## Slide 13: Basic Logic for multiplication
110100 = 52 Multiplicand 0001 = 1 Multiplier 1101= 13 Result
1) Shift the multiplier to the right.
2) If CF=1 add the multiplicand to the result.
3) Shift the multiplicand to the left.
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
CF = 1
Multiplier
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
Result
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0
Multiplicand
1
65
104

## Slide 14: Multiplication Code
; 4bit multiplication algorithm
[org 0x100]
jmp start
multiplicand: db 13 ; 4bit multiplicand (8bit space)
multiplier: db 5 ; 4bit multiplier
result: db 0 ; 8bit result
start:
mov cl, 4 ; initialize bit count to four
mov bl, [multiplicand] ; load multiplicand in bl
mov dl, [multiplier] ; load multiplier in dl

## Slide 15
checkbit: shr dl, 1 ; move right most bit in carry
jnc skip ; skip addition if bit is zero
add [result], bl ; accumulate result
skip: shl bl, 1 ; shift multiplicand left
dec cl ; decrement bit count
jnz checkbit ; repeat if bits left
mov ax, 0x4c00 ; terminate program
int 0x21

## Slide 16: Extended Operations
We have seen multiplication of two 4 bit numbers our answer is a 8 bit number.
Means if we want to multiply two 8 bit numbers our answer will be a 16 bit number.
Similarly if we want to multiply two 16 bit numbers our answer will be a 32 bit number.
But, we need to notice a thing we have done a shift left operation in our multiplication algorithm, so if we have a 16 bit multiplicand and we perform a shl operation our multiplicand should changed into a 17 bit number. But our register are 16 bit, so we need an extended shift operation.
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
We need to store 17th bit, do not drop it

## Slide 17: Extended Shifting
Our number is 40000 [fit in 16 bits] in decimal, Because of our architecture limitation we can use only 16 bit register. We can save 40000 in a register but can shift left using a register.
We need some space in memory to store our shifted number.
Original number is 16 bit, shifted can be 32 bit so we need 32 bit space.
num1: dd 40000
dd means define double. Declare or reserve 32 bits in memory for num1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0X00009C40 in hex

## Slide 18: Extended Shifting
 | 8 bits | 8 bits | 8 bits | 8 bits
DS:0000 | 40 | 9C | 00 | 00
num1: dd 40000
0000 9C40 in hex
num1
num1 + 2

## Slide 19: Extended Shift Left
40 | 9C
Shift Left
CF
0 | 0
0
num1
num1 + 2
Rotate Through Cary Left
CF

## Slide 20: Extended Shifting
 | 8 bits | 8 bits | 8 bits | 8 bits
DS:0000 | 40 | 9C | 00 | 00
num1: dd 40000
0000 9C40 in hex
num1
num1 + 2

## Slide 21: Extended Shift Right
40 | 9C
CF
0 | 0
0
num1
num1 + 2
CF
Shift right
Rotate through Carry Right

## Slide 22: Extended Shl and Shr
Shl
num1: dd 40000
shl word [num1], 1
rcl word [num1+2], 1
Shr
num1: dd 40000
shr word [num1+2], 1
rcr word [num1], 1

## Slide 23: Extended Addition and Subtraction
 | 8 bits | 8 bits | 8 bits | 8 bits
DS:0000 | 40 | 9C | 00 | 00
dest: dd 40000 00009C40 in hex
dest
dest + 2
src: dd 80000
00013880 in hex
 | 8 bits | 8 bits | 8 bits | 8 bits
DS:0000 | 80 | 38 | 01 | 00
src
Src + 2

## Slide 24: Extended Addition
src 0001 3880 in hex
Dest 0000 9C40 in hex
  ___________________
    Final Answer
dest: dd 40000
src: dd 80000
mov ax, [src]
add word [dest], ax
mov ax, [src+2]
adc word [dest+2], ax
Carry
+
+
Notes: adc means perform add operation between source and destination and also involve carry flag while addition

## Slide 25: Extended Addition
src 0001 3880 in hex
Dest 0000 9C40 in hex
  ___________________
    Final Answer
dest: dd 40000
src: dd 80000
mov ax, [src]
sub word [dest], ax
mov ax, [src+2]
sbb word [dest+2], ax
Barrow
-
-
Notes: sbb means if the lower halves needed a
borrow, a one is subtracted from the upper halves.

## Slide 26: Extended Multiplication Code
; 16 bit multiplication algorithm
[org 0x100]
jmp start
multiplicand: dd 1300 ; 16bit multiplicand (32 bit space)
multiplier: dw 500 ; 16 bit multiplier
result: dd 0 ; 32 bit result
start:
mov cl, 16 ; initialize bit count to sixteen
mov dx, [multiplier] ; load multiplier in dx

## Slide 27
checkbit: shr dx, 1 ; move right most bit in carry
jnc skip ; skip addition if bit is zero
mov ax, [multiplicand]
add [result], ax ; add less significant word
mov ax, [multiplicand+2]
adc [result+2], ax ; add more significant word
skip: shl word [multiplicand], 1
rcl word [multiplicand+2], 1
dec cl ; decrement bit count
jnz checkbit ; repeat if bits left
; terminate program
Extended addition
;Extended shift multiplicand left