## Slide 1: Computer Organization and Assembly Fall 2019
Lecture 9
Syeda Farwa Batool

## Slide 2: Shift Arithmetic Left (SAL) and
1 | 1 | 0 | 1 | 1 | 0 | 1 | 0
CF = 0
This was last bit which dropped from left also copied in carry flag

## Slide 3: BITWISE LOGICAL OPERATIONS
AND
    mov ax,10
    and ax,0 ;; now ax is 0
OR
    mov ax,10
    or ax,0 ;; now ax is 0
    or byte [num] , 5
XOR
    mov ax,10
    XOR ax,ax ;; now ax is 0
NOT
    mov ax,10
    not ax ;; now ax is 5

## Slide 4: Masking Operations
Selective Bit Clearing
Use AND operator such that The source operand is loaded with a mask containing one at positions which are retain their old value and zero at positions which are to be zeroed.
For Example
Al = 00001001 ;and we want to clear right most bit
Then Mask = 11111110
and byte al, [mask] ;; now Al has 00001000

## Slide 5
Selective Bit Setting
Use OR operator such that The source operand is loaded with a mask, The bits in the mask are cleared at positions which are to retain their values, and are set at positions which are to be set.
For Example
Al = 00001001 ;and we want to set second and third bit from right
Then Mask = 00000110
or byte al, [mask] ;; now Al has 00001111

## Slide 6
Selective Bit Inversion
Use OR operator such that The source operand is loaded with a mask, The bits in the mask are cleared at positions, which are to retain their values, and are set at positions, which are to be inverted.
For Example
Al = 00001001 ;and we want to invert second nibble bits
Then Mask = 11110000
xor byte al, [mask] ;; now Al has 11111001

## Slide 7
Selective Bit Testing
AND can be applied on a destination with a 1-bit in the desired position and a source, which is to be checked. If the destination is zero as a result, which can be checked with a JZ instruction, the bit at the desired position in the source was clear.
For Example
Al = 00001001 ;and we want test right most bit
Then Mask = 00000001
and byte [mask], al ;; now mask has 00000001 means right most bit is set
TEST instruction and is a non-destructive AND operation. It doesn’t change the destination and only sets the flags according to the AND operation.